## Slide 1: Early housing scheme – not yet completed
Bill Blackledge CMLI
Susdrain SuDS Theatre, Floodex
27/11/2024

## Slide 2
Bill Blackledge CMLI

## Slide 3
Wellbank Park Self-build Housing, Cumbria

## Slide 9
Landscape Design
Sustainable Drainage
Biodiversity (Net Gain)
Save money
Help sales
Satisfy regulation
Climate mitigation
Multifunctional
Better places
…Unlock development

## Slide 10
Project image here

## Slide 14
Swales for conveyance only – no attenuation
Cellular storage
No use of landscape apart from ponds – still deep
Limited by assumptions as to adoptability by Highways / UU (and no time/scope to enter into discussions with them)
Time to give up?

## Slide 15
Swales with attenuation
Shallow highway crossings allows connections between plots + highway swales
Permeable paving
Shallow-edge ponds with defined levels
Use of landscape
Contours!

## Slide 16
Key Principles:
Keeping water at, or as close to, the surface as possible, with shallow sides-slopes and depths for maximum safety
Minimising underground pipework and drainage
Distributed collection and attenuation of rainwater and use of swales for conveyance (source control and bio-filtration)
Multi-functional uses, e.g. surface water conveyance and attenuation, amenity, play, biodiversity – noting that source control and bio-filtration will result in cleaner water in swales and pond.
To satisfy, as far as possible, the 'four pillars of SuDS' (CIRIA SuDS Manual and potential revised National SuDS Standards): water quantity, water quality, amenity and biodiversity.
All attenuation/conveyance features (except ponds) are to be designed for controlled drain-down over 24-48 hours after a storm event, resulting in normally-dry swale/basin features. Legibility of SuDS function enhanced by choice of edge planting and use of local cobbles/rocks giving 'dry stream' effect.
Site subsoil is effectively impermeable, so no infiltration is assumed. All SuDS features drain by gravity, via control features, to lowest point of site and thence to outfall manhole.

## Slide 17
SuDS Examples

## Slide 18
“Priority must be given to the use of sustainable drainage systems (SuDS).
Sustainable Drainage Systems (SuDS) mimic natural drainage patterns and provide water quantity (flooding), water quality (pollution), amenity and biodiversity benefits. The SuDS manual C753 (published by CIRIA) provides guidance on the planning, design, construction and maintenance of SuDS.”

## Slide 19
Two major changes:
Client decided to create management company (worked with community features such as the Community Hub) – so no adoption issues…
New engineer appointed

## Slide 30: Thanks for listening!
Bill Blackledge
2B Landscape Consultancy Ltd
bill@2bconsultancy.co.uk
www.2bconsultancy.co.uk
https://www.linkedin.com/company/2b-landscape-consultancy-ltd
https://www.instagram.com/2b_landscape/
Susdrain SuDS Theatre, Floodex
27/11/2024